## Slide 1: Sensors Challenge Overview
Joe Davies, PhD
Quantinuum, LLC.

## Slide 2: Introduction
Sensors challenge history
  2nd sensors challenge
  Proposed by Prof. Victorino Franco (Univ. of Sevilla)
  First challenge
    Joint MMM meeting, January 2022, New Orleans
    Six participants
Goals
  Give more practical/applied experience in sensors
  Use sensors + teamwork + creativity to utilize sensors
  Network and have fun in the process!

## Slide 3: Sensor Technologies
Technology | Detectivity (pT/√Hz @1Hz) | Optimal Speed | Volume (cm3) | Power | Cost | CMOS Integrable
TMR | 10 | Hz – kHz | 1e-5 | uW | <$ 1 | Yes
GMR | 100 | Hz – MHz | 1e-5 | mW | <$ 1 | Yes
AMR | 100 | Hz – MHz | 1e-4 | mW | <$ 1 | Yes
Hall | 30,000 | Hz – kHz | 1e-4 | mW | $ 0.1 | Kind-of
Fluxgate | 1 | Hz | 1 | W | 0.1 k$ | No
Vapor | 0.01 | Hz | 1 | W | 1 k$ | No
Squid | 0.001 | Hz | 0.5 | W | >1 k$ | No
Rough order of magnitude estimates
TMR/GMR Market driven by best performance for small size, low power and cost

## Slide 4: Device configurations
Magnetic property tailoring enables different device types
Field
Resistance
Digital
Strong uniaxial anisotropy
Memory/Switches
Unipolar
Bipolar
Cross-axis anisotropy
Magnetometry
Current sensing
Navigation
Multilayer stack
Proximity sensing
Unipolar switches

## Slide 5: Typical Sensor, CIP GMR
Wheatstone bridge
  Excellent temperature stability
Two “reference” legs
  Shields or “dead” GMR
Flux concentrate “active” legs
Example: linear response, 10% GMR, Saturate at 10 Oe
 8.2 mV/V-Oe sensitivity

## Slide 6: Field and Frequency Marketspace
Industrial controls/positioning
Geophysical
Magnetic Anomalies
Magneto-cardiography/ Encephalography
HDD/data storage
Adapted from “Magnetic Sensors and Magnetometers”, P. Ripka, Artech, (2001)
Hall Sensors
GMR
TMR
Flux Gate
Atomic/Vapor Magnetometer, SQUIDs
AMR
STT, STO, STMD
Increasing Cost

## Slide 7: Sensor Marketspace
Mechanical position sensing
  Cylinder positioning, flow meters, geartooth sensors, encoders
Magnetic field anomaly detection
  Medical devices/biosensors
  Defect/particle detections
Electric current sensing
  Electric vehicles, precision motor/power control

## Slide 8: Applications
  Medical device sensors (e.g., pacemakers and hearing aids)
  Biomagnetics/particle detection
  Anomaly detection (e.g., vehicles)
  Compassing
  Speed, position, and angle sensors
  Data storage
  Current sensors
  Security
Implantable
Cardiac Defibrillator

## Slide 9
Interesting Case study: Implant Reliability
Guidant (Boston Scientific) pacemaker recalled due to mechanical reed switch “stickage”
Magnetoresistive switches save the day
Photo: “A recalled Guidant defibrillator,” StarTribune, 8/7/05

## Slide 10: The Challenge
Find an interesting way to utilize sensors
Present solution as a Tiktok video
  #mmmsensorschallenge2022

## Slide 11: Sensors
Magnets
Unipolar GMR Sensor
3-axis AMR compass sensor
Hall Digital Switch

## Slide 12: Arduino Kit
Lots of extras for the project
Need Arduino IDE for programming
“ReadAnalogVoltage” example is good starting point

## Slide 13: Tiktok Submission
Submit Tiktok videos by 8pm-ish Thursday
Use #2022mmmsensorchallenge for people to find
Panel of chairs will view and judge a winner
All will be recognized in upcoming IEEE magnetics society news letter and awards/plenary session
Sensors and kits are for the teams to keep

## Slide 14: Resources
Room is available each evening for meeting
  Not required to use
Arduino:
  https://www.arduino.cc/en/Guide
Sensor use:
  NVE GMR sensor
    https://www.nve.com/analogSensors
  Hall Effect Sensor: Gikfun A3144/OH3144/44E/AH3144E
    https://youtu.be/4-MB1jBocW4
  AMR compass (I2C communication)
    https://electropeak.com/learn/interfacing-gy-271-hmc5883l-compass-magnetometr-with-arduino/